## Slide 1
Inducing Data Loss in Zigbee Networks via Join/Association Handshake Spoofing
Introduction
Problem
Spoofing the Coordinator
Proposed solution
Experimental Evaluation and Results
Given a Zigbee network composed of a coordinator (root) node and one or more child devices, and assuming that we cannot overcome the network's encryption, our goal is to induce loss of the data transmitted from an end device to the coordinator. As a secondary goal, we will propose a low-overhead countermeasure to our attack.
Many denial-of-service attacks, e.g. jamming or flooding, are straightforward and effective, but easily detectable. Our attack should not be readily apparent to the owners of the network, minimizing the amount of abnormal activity perceived by other devices.
Spoofing the coordinator is possible since all packets in the join/association handshake are unencrypted.
Zigbee is a popular IEEE 802.15.4-based specification for low-power mesh networks, frequently used for infrastructure control and monitoring
Zigbee’s ad-hoc network establishment and low power requirements seriously limit its security measures, creating a variety of attack possibilities
Attack Overview
Acquire network information
  Our fake node masquerades as a new device and issues a beacon request to get network information from the coordinator
Prevent a new device from discovering the network
  Wait for a beacon request from a new device; corrupt it by jamming so the coordinator does not reply with network info.
Spoof the coordinator on another channel
  Switch to a different channel (so as not to be noticed by the original network) and use information from step 1 to spoof the controller and carry out a handshake with the new device
Conclusion
Spencer Michaels, Kemal Akkaya, A. Selcuk Uluagac Elect. & Comp. Engineering, Florida International University smichaels@hmc.edu, {kakkaya,uluagac}@fiu.edu
All information needed to spoof can be obtained without breaking the network’s encryption
Beacon request
2. Beacon
3. Assoc. request
4. Assoc. response
Joining device
Coordinator
Joining device
Coordinator
2.
4. Jam,
then switch
channel
to Y
6. Beacon 5. Beacon request
8. AscRsp.+ACK 7. AscReq.
9. Data requests
10. ACKs
Channel X
Channel Y
Beacon
+ link status
3. Beacon request
Beacon request
The end device caches recently transmitted data. When the cache is full, it sends a challenge to the coordinator, encrypted using the network key (which, by our assumptions, the rogue node does not know).
If the response is wrong/absent, the end device leaves, restarts the assoc. process, and resends cached data. If correct, it clears cache and continues.
Packet #1 (cache 1 / N)
End device
Coordinator
Pkt 1
Pkt N
Cache
...
Packet #N (cache N / N)
Challenge
Response
Packet #(N+1) (cache 1 / N)
[ Cache cleared ]
...
P. N+1
...
...
clear
Rogue node
We consider the handshake spoof successful if the end device sends data requests to the rogue node afterward (step 9 at left). This does indeed occur.
  In order to facilitate the complete Wireshark capture below, the channel switch does not occur. Instead, the coordinator was manually switched off after step 2, producing the same effect as if steps 3 and 4 had occurred.
1.
2.
5.
6.
6.
7.
8.
9.
10.
5.
3./4.*
Because our own node’s hardware could not respond quickly enough to reliably ACK data requests, the connection only lasted for roughly a second.
Using a simulator, a preliminary implementation of the challenge-response system proved workable.
The handshake-spoofing attack does succeed.
  However, hardware limitations prevented us from determining how long the end device can feasibly be kept connected
The challenge-response method has the potential to be an effective countermeasure.
  If the end device’s memory permits a reasonably sized cache, the network resource cost will be low under normal conditions
Notes: 1